## Slide 1: Computer Organization and Architecture
System Buses

## Slide 2: Program Concept
Hardwired systems are inflexible
  General purpose hardware can do different tasks, given correct control signals
  Instead of re-wiring, supply a new set of control signals
Programs
  Sequence of steps
  For each step, an arithmetic or logical operation is done
  For each operation, a different set of control signals is needed

## Slide 3: Function of Control Unit
For each operation a unique code is provided
  e.g. ADD, MOVE
A hardware segment accepts the code and issues the control signals

## Slide 4: Components
The Control Unit and the Arithmetic and Logic Unit constitute(create) the Central Processing Unit
Data and instructions need to get into the system and results out
  Input/output
Temporary storage of code and results is needed
  Main memory

## Slide 5: Interactions among Computer Components: Top Level View

## Slide 6: Interactions among Computer Components
Memory Address Register (MAR) – specifies address for next read or write
Memory Buffer Register (MBR) – contains data to be written into or receives data read from memory
I/O address register (I/O AR) - specifies a particular I/O device
I/O buffer register (I/O BR) - used for exchange of data between an I/O module and CPU (or memory)
Memory module - a set of locations
  with sequentially numbered addresses
  each holds a binary number that can be either an instruction or data

## Slide 7: Execute Cycle
Program Execution

## Slide 8: Instruction Cycle
Two steps:
  Fetch
  Execute

## Slide 9: Fetch Cycle
Program Counter (PC) holds address of next instruction to fetch
Processor fetches instruction from memory location pointed to by PC
Increment PC
  Unless told otherwise
Instruction loaded into Instruction Register (IR)
Processor interprets instruction and performs required actions

## Slide 10: Execute Cycle
Processor-memory
  data transfer between CPU and main memory
Processor I/O
  Data transfer between CPU and I/O module
Data processing
  Some arithmetic or logical operation on data
Control
  Alteration of sequence of operations
  e.g. jump
Combination of above

## Slide 12: Instruction Cycle State Diagram

## Slide 13: Interrupts
Changing Program Flow

## Slide 14: Interrupts
Mechanism by which other modules (e.g. I/O) may interrupt normal sequence of processing
Program - as a result of program execution
  e.g. overflow, division by zero
Timer
  Generated by internal processor timer
  Used in pre-emptive multi-tasking
I/O - to signal completion of I/O or error
  from I/O controller
Hardware failure
  e.g. memory parity error, power failure

## Slide 15: Program Flow Control

## Slide 16: Interrupt Cycle
Added to instruction cycle
Processor checks for interrupt
  Indicated by an interrupt signal
If no interrupt, fetch next instruction
If interrupt pending:
  Suspend(hang) execution of current program
  Save context
  Set PC to start address of interrupt handler routine
  Process interrupt
  Restore context and continue interrupted program

## Slide 17: Transfer of Control via Interrupts

## Slide 18: Instruction Cycle with Interrupts

## Slide 19: Instruction Cycle (with Interrupts) - State Diagram

## Slide 20: Multiple Interrupts
Two approaches can be taken to dealing with multiple interrupts
Disable interrupts
  Processor will ignore further interrupts whilst processing one interrupt
  Interrupts remain pending and are checked after first interrupt has been processed
  Interrupts handled in sequence as they occur
Define priorities
  Low priority interrupts can be interrupted by higher priority interrupts
  When higher priority interrupt has been processed, processor returns to previous interrupt
The drawback to the preceding approach is that it doesn’t take into account relative priority or time-critical needs.

## Slide 21: Multiple Interrupts - Sequential

## Slide 22: Multiple Interrupts – Nested

## Slide 23: Time Sequence of Multiple Interrupts

## Slide 24: Busses
Connecting Components

## Slide 25: Connecting
The collection of paths connecting the various modules of a computer (CPU, memory, I/O) is called the interconnection structure.
All the units must be connected
Different type of connection for different type of unit
  Memory
  Input/output
  CPU

## Slide 26: Computer Modules
Address
Data Read
Data Write
Interrupt Signals

## Slide 27: Computer Modules
It must support the following types of transfers:
  Memory to CPU – the processor read an instruction or a unit of data from memory.
  CPU to Memory – the processor writes a unit of data to memory.
  I/O to CPU – the processor read data from an I/O devices via an I/O module.
  CPU to I/O – the processor sends data to the I/O devices.
  I/O to or from Memory – For these two cases, an I/O module is allowed to exchange data directly with memory, without going through the processor, using Direct Memory Access (DMA)

## Slide 28: Memory Connection
Receives and sends data
Receives addresses (of locations)
Receives control signals
  Read
  Write
  Timing

## Slide 29: Input/Output Connection(1)
Similar to memory from computer’s viewpoint
Output
  Receive data from computer
  Send data to peripheral
Input
  Receive data from peripheral
  Send data to computer

## Slide 30: Input/Output Connection(2)
Receive control signals from computer
Send control signals to peripherals
  e.g. spin disk
Receive addresses from computer
  e.g. port number to identify peripheral
Send interrupt signals (control)
External data line is used to communicate between I/O module and peripherals
Internal data line is used to communicate between I/O module and CPU/Memory

## Slide 31: CPU Connection
Reads instruction and data
Writes out data (after processing)
Sends control signals to other units
Receives (& acts on) interrupts

## Slide 32: Buses
There are a number of possible interconnection systems
Single and multiple BUS structures are most common
e.g. Control/Address/Data bus (PC)
e.g. Unibus (DEC-PDP)

## Slide 33: What is a Bus?
A communication pathway connecting two or more devices
Characteristics
  It is a shared transmission medium.
      Must only be used by one device at a time
      When used to connect major computer components (CPU, memory, I/O) is called a system bus.
Usually broadcast
Often grouped
  A number of channels in one bus
  e.g. 32 bit data bus is 32 separate single bit channels
Power lines may not be shown

## Slide 34: Data Bus
Carries data
  Remember that there is no difference between “data” and “instruction” at this level
Width is a key determinant of performance
  8, 16, 32, 64 bit

## Slide 35: Address bus
Identify the source or destination of data
e.g. CPU needs to read an instruction (data) from a given location in memory
Bus width determines maximum memory capacity of system
  e.g. 8080 has 16 bit address bus giving 64k address space

## Slide 36: Control Bus/Line
Control access to and use of the data and address lines. Typical control lines include:
  Memory Read and Memory Write
  I/O Read and I/O Write
  Transfer ACK
  Bus Request and Bus Grant
  Interrupt Request and Interrupt ACK
  Clock
  Reset

## Slide 37: Bus Interconnection Scheme

## Slide 38: Big and Yellow?
What do buses look like?
  Parallel lines on circuit boards
  Ribbon cables
  Strip connectors on mother boards
    e.g. PCI
  Sets of wires

## Slide 39: Physical Realization of Bus Architecture

## Slide 40: Single Bus Problems
A great number of devices on a bus will cause performance to suffer
  Propagation delay - the time it takes for devices to coordinate the use of the bus
  The bus may become a bottleneck as the aggregate data transfer demand approaches the capacity of the bus (in available transfer cycles/second)
Most systems use multiple buses to overcome these problems

## Slide 41: Traditional (with cache)

## Slide 42: Traditional Hierarchical Bus Architecture
Use of a cache structure insulates CPU from frequent accesses to main memory
Main memory can be moved off local bus to a system bus
Expansion bus interface
  buffers data transfers between system bus and I/O controllers on expansion bus
  insulates memory-to-processor traffic from I/O traffic

## Slide 43: High Performance Bus

## Slide 44: High-performance Hierarchical Bus Architecture
Traditional hierarchical bus breaks down as higher and higher performance is seen in the I/O devices
Incorporates a high-speed bus
  specifically designed to support high-capacity I/O devices
  brings high-demand devices into closer integration with the processor and at the same time is independent of the processor
  Changes in processor architecture do not affect the high-speed bus, and vice versa
Sometimes known as a mezzanine architecture

## Slide 45: Bus Types
Dedicated - a line is permanently assigned either to one function or to a physical subset of computer components
Multiplexed
  Time multiplexing - using the same lines for multiple purposes (different purposes at different times)
  Uses fewer lines, saving space and cost
  BUT more complex circuitry required in each module
  BUT potential reduction in performance
Physical dedication - the use of multiple buses, each of which connects to only a subset of modules, with an adapter module to connect buses and resolve contention at the higher level.

## Slide 46: Bus Types
Dedicated
  Separate data & address lines
Multiplexed
  Shared lines
  Address valid or data valid control line
  Advantage - fewer lines
  Disadvantages
    More complex control
    Ultimate performance

## Slide 47: Bus Arbitration
More than one module controlling the bus
e.g. CPU and DMA controller
Only one module may control bus at one time
Arbitration may be centralised or distributed

## Slide 48: Centralised or Distributed Arbitration
Centralised
  Single hardware device controlling bus access
    Bus Controller
    Arbiter
  May be part of CPU or separate
Distributed
  Each module may claim the bus
  Control logic on all modules

## Slide 49: Method of Arbitration
Determining who can use the bus at a particular time
  Centralized - a single hardware device called the bus controller or arbiter allocates time on the bus
  Distributed - each module contains access control logic and the modules act together to share the bus
  Both methods designate one device (either CPU or an I/O module) as master, which may initiate a data transfer with some other device, which acts as a slave.

## Slide 50: Timing
Control Action w.r.t Time Signal

## Slide 51: Timing
Co-ordination of events on bus
Synchronous
  Events determined by clock signals
  Control Bus includes clock line
  A single 1-0 is a bus cycle
  All devices can read clock line
  Usually sync on leading edge
  Usually a single cycle for an event

## Slide 52: Synchronous Timing
  Control Bus includes clock line.
  Clock transmits a regular sequence of alternating 1’s and 0’s of equal duration
A single 1-0 transmission is referred to as a clock cycle or bus cycle
All other devices on the bus can read the clock line, and all events start at the beginning of a clock cycle

## Slide 53: Asynchronous Timing
The occurrence of one event on a bus follows and depends on the occurrence of a previous event
Allows system to take advantage of advances in device performance by having a mixture of slow and fast devices, using older and newer technology, sharing the same bus
BUT harder to implement and test than synchronous timing

## Slide 54: Synchronous Timing Diagram (Read)
Control Signals
Address
Data Read
Step 1
Step 2
Step 3
Step 4
Step 6
Step 5

## Slide 55: Synchronous Timing Diagram (Write)
Control Signals
Address
Data Write
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6

## Slide 56: Asynchronous Timing – Read Diagram
Control Signals
Address
Data Read
Step 1
Step 2
Step 3
Step 4
Step 5

## Slide 57: Asynchronous Timing – Write Diagram
Control Signals
Address
Data Write
Step 1
Step 2
Step 3
Step 4
Step 5