## Slide 1: Cache Memory
Structure and Function

## Slide 2: Cache Memory
A cache ( pronounced KASH) is a component that transparently stores data so that future requests for that data can be served faster.
Analogous(similar) to …
  Weapons and Food cache
  Ladies hand bag
  A students journal (notes)
Cache Hit
  If requested data is contained in the cache (cache hit), this request can be served by simply reading the cache, which is comparatively faster.
Cache Miss
  Otherwise the data has to be fetched from its original storage location, which is comparatively slower.
Efficiency
  Cache hits > Cache Miss

## Slide 3: Characteristics
Location
Capacity
Unit of transfer
Access method
Performance
Physical type
Physical characteristics
Organisation

## Slide 4: Location
CPU
Internal (main)
External (secondary)

## Slide 5: Capacity
Word size
  The natural unit of organisation
  typically equal to the number of bits used to represent a number and to the instruction length.
Number of words
  or Bytes
  Number of Words - has to do with the number of addressable units (which are typically words, but are sometimes bytes, regardless of word size). For addresses of length A (in bits), the number of addressable units is 2^A.

## Slide 6: Unit of Transfer
Internal
  Usually governed by data bus width
External
  Usually a block which is much larger than a word
Addressable unit
  Smallest location which can be uniquely addressed
  Word internally
  Cluster on M$ disks

## Slide 7: Access Methods (for all memory devices)
Sequential
  Start at the beginning and read through in order
  Access time depends on location of data and previous location
  e.g. tape
Direct
  Individual blocks have unique address
  Access is by jumping to vicinity(nearby area) plus sequential search
  Access time depends on location and previous location
  e.g. disk

## Slide 8: Access Methods (for all memory devices)
Random
  Individual addresses identify locations exactly
  Access time is independent of location or previous access
  e.g. RAM
Associative
  Data is located by a comparison with contents of a portion of the store
  Access time is independent of location or previous access
  e.g. cache

## Slide 9: Organization
The physical arrangement of bits to form words.
  Obvious arrangement not always used
  Ex. Characters vs. Integers vs. Floating Point Numbers

## Slide 10: Memory Hierarchy
Registers
  In CPU
Internal or Main memory
  May include one or more levels of cache
  “RAM”
External memory
  Backing store

## Slide 11: Memory Hierarchy - Diagram

## Slide 12: Hierarchy List
Registers
L1 Cache
L2 Cache
Main memory
Disk cache
Disk
Optical
Tape

## Slide 13: Access Times

## Slide 14: Cache Levels
Due to increasing gap between CPU and main Memory, small memory called L1 cache is inserted.
  L1 caches can be accessed almost as fast as the registers, typically in 1 or 2 clock cycle
  Due to even more increasing gap between CPU and main memory, Additional cache: L2 cache is inserted between L1 cache and main memory
Some high performance systems also include additional L3 cache which sits between L2 and main memory
The cache is placed both physically closer and logically closer to the CPU than the main memory.

## Slide 15: Performance
Access time
  Time between presenting the address and getting the valid data
Memory Cycle time (MCT)
  MCT (primarily for random-access memory) = access time + additional time required before a second access can begin
Transfer Rate
  Rate at which data can be transferred into or out of a memory unit. For Random-access memory, it is equal to 1/(cycle time).
  for non-random-access memory
  Tn = average time to read or write N bits, Ta = average access time
  n = number of bits, R = transfer rate, in bits per second (bps)

## Slide 16: Physical Types
Semiconductor
  RAM
Magnetic
  Disk & Tape
Optical
  CD & DVD
Others
  Bubble
  Hologram

## Slide 17: Physical Characteristics
Decay - decline in quality
Volatility - information decays or is lost when power is lost
Erasable - removable
Power consumption
non-volatile - information remains without deterioration until changed -- no electrical power needed
non-erasable
  information cannot be altered with a normal memory access cycle
  As a practical matter, must be non-volatile

## Slide 18: The Bottom Line
How much?
  Capacity
How fast?
  Time is money
How expensive?
  Cost
There are trade-offs between the 3 key characteristics of memory (cost, capacity, and access time) which yield the following relationships:
  Smaller access time -> greater cost per bit
  Greater capacity -> smaller cost per bit
  Greater capacity -> greater access time

## Slide 19: So you want fast?
It is possible to build a computer which uses only static RAM (see later)
This would be very fast
This would need no cache
  How can you cache cache?
This would cost a very large amount

## Slide 20: Locality of Reference
During the course of the execution of a program, memory references tend to cluster
e.g. loops

## Slide 21: Why is cache memory needed?
When a program references a memory location, it is likely to reference that same memory location again soon.
A memory location that is near a recently referenced location is more likely to be referenced then a memory location that is farther away.
A small but fast cache memory, in which the contents of the most commonly accessed locations are maintained, can be placed between the CPU and the main memory.
When a program executes, the cache memory is searched first.

## Slide 22: Why is cache memory fast?
Faster electronics used
A cache memory has fewer locations than a main memory, which reduces the access time
The cache is placed both physically closer and logically closer the CPU than the main memory
The cache-less computer (In Fig) usually needs a few bus cycles to synchronize the CPU with the bus.
A cache memory can be positioned closer to the CPU.

## Slide 23: Cache Structure and Operation
Cache Memory

## Slide 24: Cache
Small amount of fast memory
Sits between normal main memory and CPU
May be located on CPU chip or module

## Slide 25: Cache/Main Memory Structure

## Slide 26: Typical Cache Organization

## Slide 27: Cache Operation
Hits and Miss

## Slide 28: Cache operation - overview
CPU requests contents of memory location
Check cache for this data
If present, get from cache (fast)
If not present, read required block from main memory to cache
Then deliver from cache to CPU
Cache includes tags to identify which block of main memory is in each cache slot

## Slide 29: Cache Read Operation - Flowchart