## Slide 1: Cache Memory
Pentium Cache

## Slide 2: Pentium 4 Cache
80386 – no on chip cache
80486 – 8k using 16 byte lines and four way set associative organization
Pentium (all versions) – two on chip L1 caches
  Data & instructions
Pentium 4 – L1 caches
  8k bytes
  64 byte lines
  four way set associative
L2 cache
  Feeding both L1 caches
  256k
  128 byte lines
  8 way set associative

## Slide 3: Pentium 4 Diagram (Simplified)

## Slide 4: Pentium 4 Core Processor
Fetch/Decode Unit
  Fetches instructions from L2 cache
  Decode into micro-ops
  Store micro-ops in L1 cache
Out of order execution logic
  Schedules micro-ops
  Based on data dependence and resources
  May speculatively execute
Execution units
  Execute micro-ops
  Data from L1 cache
  Results in registers
Memory subsystem
  L2 cache and systems bus

## Slide 5: Pentium 4 Design Reasoning
Decodes instructions into RISC like micro-ops before L1 cache
Micro-ops fixed length
  Superscalar pipelining and scheduling
Pentium instructions long & complex
Performance improved by separating decoding from scheduling & pipelining
  (More later – ch14)
Data cache is write back
  Can be configured to write through
L1 cache controlled by 2 bits in register
  CD = cache disable
  NW = not write through
  2 instructions to invalidate (flush) cache and write back then invalidate

## Slide 6: Comparison of Cache Sizes