## Slide 1: Internal Memory
ROM and RAM

## Slide 2: Semiconductor Memory Types

## Slide 3: Semiconductor Memory
RAM
  Misnamed as all semiconductor memory is random access
  Read/Write
  Volatile
  Temporary storage
  Static or dynamic

## Slide 4: Memory Cell Operation
Address
Control
Data

## Slide 5: Dynamic RAM - DRAM
Bits stored as charge in capacitors
Charges leak
Need refreshing even when powered
Simpler construction
Smaller per bit
Less expensive
Need refresh circuits
Slower
Main memory
Essentially analogue
  Level of charge determines value

## Slide 6: Dynamic RAM Structure
Items | Count
Transistor | 1
Capacitor | 1

## Slide 7: Dynamic RAM Structure - READ
Address
Data

## Slide 8: Dynamic RAM Structure - WRITE
Address
Data

## Slide 9: DRAM Operation
Address line active when bit read or written
  Transistor switch closed (current flows)
Write
  Voltage to bit line
    High for 1 low for 0
  Then signal address line
    Transfers charge to capacitor
Read
  Address line selected
    transistor turns on
  Charge from capacitor fed via bit line to sense amplifier
    Compares with reference value to determine 0 or 1
  Capacitor charge must be restored

## Slide 10: Static RAM - SRAM
Bits stored as on/off switches
No charges to leak
No refreshing needed when powered
More complex construction
Larger per bit
More expensive
Does not need refresh circuits
Faster
Cache
Digital
  Uses flip-flops

## Slide 11: Static RAM Structure
Items | Count
Transistor | 6
Capacitor | NIL

## Slide 12: Static RAM Operation
Transistor arrangement gives stable logic state
State 1
  C1 high, C2 low
  T1 T4 off, T2 T3 on
State 0
  C2 high, C1 low
  T2 T3 off, T1 T4 on
Address line transistors T5 T6 is switch
Write – apply value to B & complement to B
Read – value is on line B

## Slide 13: SRAM v DRAM
Both volatile
  Power needed to preserve data
Dynamic cell
  Simpler to build, smaller
  More dense
  Less expensive
  Needs refresh
  Larger memory units
Static
  Faster
  Cache

## Slide 14: Read Only Memory (ROM)
Permanent storage
  Nonvolatile
Microprogramming or microcode
Library subroutines
Systems programs (BIOS)
Function tables

## Slide 15: Types of ROM
Written during manufacture
  Very expensive for small runs
Programmable (once)
  PROM
  Needs special equipment to program
Read “mostly”
  Erasable Programmable (EPROM)
    Erased by UV
  Electrically Erasable (EEPROM)
    Takes much longer to write than read
  Flash memory
    Erase whole memory electrically

## Slide 16: Organisation in detail
A 16 Mbit chip can be organised as 1M of 16 bit words
  A bit per chip system has 16 lots of 1Mbit chip with bit 1 of each word in chip 1 and so on
A 16 Mbit chip can be organised as a 2048 x 2048 x 4 bit array
  Reduces number of address pins
    Multiplex row address and column address
    11 pins to address (211=2048)
    Adding one more pin doubles range of values so x4 capacity

## Slide 17: Organization
1 Mbit
2048 x 2048

## Slide 18: Refreshing
Refresh circuit included on chip
Disable chip
Count through rows
Read & Write back
Takes time
Slows down apparent performance

## Slide 19: Typical 16 Mb DRAM (4M x 4)

## Slide 20: Packaging

## Slide 21: Error Correction
Hard Failure
  Permanent defect
Soft Error
  Random, non-destructive
  No permanent damage to memory
Detected using Hamming error correcting code

## Slide 22: Advanced DRAM Organization
Basic DRAM same since first RAM chips
Enhanced DRAM
  Contains small SRAM as well
  SRAM holds last line read (c.f. Cache!)
Cache DRAM
  Larger SRAM component
  Use as cache or serial buffer

## Slide 23: Synchronous DRAM (SDRAM)
Access is synchronized with an external clock
Address is presented to RAM
RAM finds data (CPU waits in conventional DRAM)
Since SDRAM moves data in time with system clock, CPU knows when data will be ready
CPU does not have to wait, it can do something else
Burst mode allows SDRAM to set up stream of data and fire it out in block

## Slide 24: SDRAM

## Slide 25: DDR SDRAM
SDRAM can only send data once per clock
Double-data-rate SDRAM can send data twice per clock cycle
  Rising edge and falling edge