## Slide 1: Replacement Analysis

## Slide 2
Depreciation is concerned with the value of an item of equipment after it has been in use for some time.
People in business need to calculate these values for taxation and replacement purposes.
What is depreciation?

## Slide 3
Book value is the value of an item to a company.
It is not the purchase price, or the replacement price, but what the item is currently worth.
Once the item has reached the stage where it can no longer be used profitably by the company then it is sold off.
The price that the item is expected to fetch is called the scrap value of the item.
Vocabulary

## Slide 4
There are three methods of determining the depreciated or book value:
    unit cost
    flat rate
    reducing balance
How do we calculate depreciation?

## Slide 5
Unit cost depreciation means that depreciation is calculated on the basis of the amount an item has been used.
For example, the value of a car can be determined by the number of kilometres it has traveled.
This differs from both flat rate and reducing balance depreciation, which are based on the age of the item.-*
What is unit cost depreciation?

## Slide 6
After 3 years the taxi will have traveled 450000 km
The depreciation incurred is:
The book value of the taxi is thus:
How do we calculate unit cost depreciation?
A company purchases a taxi for $60000. It depreciates at a rate of 5 cents per km. How much is it worth after 3 years, if the taxi travels on average 150000km per year?

## Slide 7
What is flat rate depreciation?
Flat rate depreciation is when the value of the item is reduced by a constant percentage of its original value each year.
It is quite equivalent to the concept of simple interest, except we reduce by a constant amount each year, rather than increase.
Thus, flat rate depreciation results in a linear relationship between the value of the item and its age.

## Slide 8
How do we calculate flat balance depreciation?
Suppose we purchase an item for $5000, and we depreciate it by 10% of the purchase price per annum. How much is it worth after 4 years?
4500
4000
3500
3000
We can see that the value is reducing by a steady $500 per year

## Slide 9
How do we calculate flat rate depreciation?
Thus, depreciation of 10% per annum means an annual depreciation of $500 each year:
Thus after four years the value of the item is:

## Slide 10
How do we calculate flat rate depreciation?
We can use these calculations to find a formula for flat rate depreciation:
This is the amount of time the item has been in use. We will give it the symbol t.
This is the depreciated value of the item.
We will give it the symbol V.
This is the purchase price of the item. We will give it the symbol P.
This is the rate of depreciation per annum, we will give it the symbol r (rate)
P
P
r
t
V

## Slide 11
Flat rate depreciation can be calculated using the rule:
How do we calculate flat rate depreciation?

## Slide 12
From the graph the linear relationship between the value and the age of the item is clear.
The relationship between the flat rate value of the item and its age can also be shown graphically.
$4500
$4000
$3500
$3000
We can also see that using this method eventually the item is worth nothing!!
$0

## Slide 13
What is reducing balance depreciation?
Reducing balance depreciation is when the value of the item is reduced each by a constant percentage of its value the previous year.
It is equivalent to the concept of compound interest interest, except we reduce by a constant percentage each year, rather than increase.
Thus, reducing balance depreciation results in a non-linear relationship between the value of the item and its age.

## Slide 14
How do we calculate reducing balance depreciation?
Suppose we purchase an item for $5000, and we depreciate it by 10% of the previous years value per annum. How much is it worth after 4 years?
4500
4050
3645
3280.50

## Slide 15
Reducing balance depreciation can be calculated using the rule:
How do we calculate reducing balance depreciation?

## Slide 16
The relationship between the reducing balance value of the item and its age can also be shown graphically.
From the graph the non-linear relationship between the value and the age of the item is clear.
$4500
$4050
$3645
$3280.50
And we see that the value will never actually reach $0 here.

## Slide 17
To compare flat rate with reducing balance depreciation we can graph the value against year for both types of depreciation on the same graph.
The difference between depreciated values under the different schemes increases with time.
Difference between flat rate and reducing balance after six years
Difference between flat rate and reducing balance after nine years
Comparison
After the first year, reducing balance depreciation is less than the flat rate depreciation.

## Slide 18: Replacement Analysis

## Slide 19
Make investments that are economically justified
“If you need a new machine and don’t buy it, you pay for it without ever getting it.”
Henry Ford

## Slide 20: Vital decision
When should a new dumper truck replace the existing truck?
When should a process be redesigned?
When should a product be redesigned?
The most common question asked in industry is when should the existing be replaced?

## Slide 21: Replacement Analysis
Should the existing equipment be retained or replaced?
The “Defender” is the existing equipment.
The “Challenger” is the best available replacement equipment.
If the defender proves more economical, it will be retained. If the challenger proves more economical, it will be installed.

## Slide 22: The Replacement Problem
Engineers replace the existing due to:
  Obsolescence - technological change.
  Depletion - loss of market value.
  Deterioration - wear that is overly expensive to repair.
Shall the defender be replaced now or be maintained for one or more periods.

## Slide 23: The Replacement Problem
Obsolescence occurs when an asset’s technology is surpassed by newer and/or different technologies (PC)
Depletion is the gradual loss of market value of an asset as it is being consumed or exhausted (Oil well, Timber)
Deterioration is the general loss in value of an asset due to aging process (Production machinery)

## Slide 24: Various cases of replacement
No Replacement of an existing asset (getting rid of it)
Replacement of an asset with another identical asset
Replacement of an asset with another not identical asset

## Slide 25: Issues (Consider Before Starting)
Is it morally or ethically right to do this project?
If a unit fails, must it be removed permanently from service? Or repaired? Are standby units available if the system should fail?
Do components or units fail independently of the failure of other components?
Is there a budget constraint?
In the event that the unit can be repaired after failure is their a constraint on the capacity of the repair facility?

## Slide 26: Issues (Continued)
Is there only one replacement allowed over the planning horizon? Are subsequent replacements allowed at any time during the study period?
Is their more than one replacement unit (price and quality combination) available at a given point in time?
Do future replacement units differ over time? Are technological improvements considered?
Is preventative maintenance included in the model?

## Slide 27: Issues (Continued)
Are periodic operating and maintenance costs constant or variable over time?
Are consequences other than economic impacts, i.e., sociotechnical issues considered?
Is “inflation” considered?

## Slide 28: What Is the Basic Comparison?
Identify the defender and the best challenger.
  Product.
  Machine.
  Process.
  Personnel.
  Mix.
Decision Criteria leads to one of the following:
If the defender is more economical, it should be retained.
If the challenger is more economical, it should be installed.

## Slide 29: Minimum Cost Life of the Challenger
Calculate the costs for each value of the useful life (e.g., n = 1, n = 2, n = 3, etc.)
The number of years at which the cost is minimized is the economic useful life
Costs to be considered:
  initial cost
  maintenance cost
  operating cost

## Slide 30
Replace when the marginal cost of ownership of the defender is more than that of the challenger.
Defender Marginal costs are increasing