## Slide 1
LECTURE # 3

## Slide 2: Number Representation and Computer Accuracy
Number Representation
Normalized Floating Point Representation
Rounding and Chopping

## Slide 3: Representing Real Numbers
You are familiar with the decimal system
Decimal System Base =10 , Digits(0,1,…9)
Standard Representations

## Slide 4: Fractional Binary Numbers
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
bi
bi–1
b2
b1
b0
b–1
b–2
b–3
b–j
• • •
• • •
.
1
2
4
2i–1
2i
• • •
• • •
1/2
1/4
1/8
2–j

## Slide 5: Frac. Binary Number Examples
Value Representation
  5-3/4 101.112
  2-7/8 10.1112
  63/64 0.1111112
Observations
  Divide by 2 by shifting right
  Multiply by 2 by shifting left
  Numbers of form 0.111111…2 just below 1.0
    1/2 + 1/4 + 1/8 + … + 1/2i + …  1.0
    Use notation 1.0 – 

## Slide 6: Representable Numbers
Limitation
  Can only exactly represent numbers of the form x/2k
  Other numbers have repeating bit representations
Value Representation
  1/3 0.0101010101[01]…2
  1/5 0.001100110011[0011]…2
  1/10 0.0001100110011[0011]…2

## Slide 7: 7-Bit Representation (sign: 1 bit, Mantissa 3bits,exponent 3 bits)

## Slide 8: Example
9 bit-hypothetical word
the first bit is used for the sign of the number,
the second bit for the sign of the exponent,
the next four bits for the mantissa, and
the next three bits for the exponent
We have the representation as
0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1
Sign of the number
mantissa
Sign of the exponent
exponent

## Slide 9: Representation
Hypothetical Machine (using 6 bits to rep number)
Mantissa 3 bits exponent 2 bit sign 1 bit
Possible machine numbers
.25 .3125 .375 .4375 .5 .625 .75 .875
1 1.25 1.5 1.75

## Slide 10: Representation
Gap near zero

## Slide 11
Mantissa | Exponent |  |  |  |  |  | 
 | n= -3 | n= -2 | n= -1 | n=0 | n=1 | n=2 | n=3
0.1000 | .0625 | .125 | .25 | .5 | 1 | 2 | 4
.1001 | .0703125 | .140625 | .28125 | .5625 | 1.125 | 2.25 | 4.5
.1010 | .078125 | .15625 | .3125 | .625 | 1.25 | 2.5 | 5
.1011 | .0859375 | .171875 | .34375 | .6875 | 1.375 | 2.75 | 5.5
.1100 | .09375 | .1875 | .375 | .75 | 1.5 | 3 | 6
.1101 | .1015625 | .203125 | .40625 | .8125 | 1.625 | 3.25 | 6.5
.1110 | .109375 | .21875 | .4375 | .875 | 1.75 | 3.5 | 7
.1111 | .1171875 | .234375 | .46875 | .9375 | 1.875 | 3.75 | 7.5

## Slide 12
Machine Epsilon
Defined as the measure of accuracy and found by difference between 1 and the next number that can be represented
Notes: THG picture

## Slide 13: Remarks
Numbers that can be exactly represented are called machine numbers
Difference between machine numbers is not uniform
sum of machine numbers is not necessarily a machine number
0.25 + .3125 =0.5625 (not a machine number)

## Slide 14
IEEE 754 STANDARDS

## Slide 15: Floating Point Representation
Numerical Form
  (-1)s M 2E
    Sign bit s determines whether number is negative or positive
    Significand M normally a fractional value in range [1.0,2.0).
    Exponent E weights value by power of two
Encoding
  MSB is sign bit
  exp field encodes E
  mantissa field encodes M
s
exp
mantissa

## Slide 16: Floating Point Precisions
Encoding
  MSB is sign bit
  exp field encodes E
  Mantissa field encodes M
Sizes
  Single precision: 8 exp bits, 23 mantissa bits
    32 bits total
  Double precision: 11 exp bits, 52 mantissa
  bits
    64 bits total
s
exp
mantissa

## Slide 17: IEEE-754 Format Single Precision
17
32 bits for single precision
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sign
(s)
Biased
Exponent (e’)
Mantissa (m)

## Slide 18: Example
18
1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sign
(s)
Biased
Exponent (e’)
Mantissa (m)

## Slide 19: “Normalized” Numeric Values
Condition
  exp  000…0 and exp  111…1
Exponent coded as biased value
  E = Exp – Bias
    Exp : unsigned value denoted by exp
    Bias : Bias value
      Single precision: 127 (Exp: 1…254, E: -126…127)
      Double precision: 1023 (Exp: 1…2046, E: -1022…1023)
Significand coded with implied leading 1
  M = 1.xxx…x2
    xxx…x: bits of fraction
    Minimum when 000…0 (M = 1.0)
    Maximum when 111…1 (M = 2.0 – )
    Get extra leading bit for “free”

## Slide 20: Normalized Encoding Example
Value
  Float F = 15213.0;
  1521310 = 111011011011012 = 1.11011011011012 X 213
Significand
  M = 1.11011011011012
  frac = 110110110110100000000002
Exponent
  E = 13
  Bias = 127
  Exp = 140 = 100011002

## Slide 21: Rounding and Chopping
Rounding: Replace the number by the nearest machine number
Chopping: Throw all extra digits