## Slide 1: Computer Networks Course Code CPS-422 WIRESHARK
Lab 03
Demonstrator Kabeer Ahmed
MS Telecommunication and Networks from Iqra University

## Slide 2: Aim
Students will learn the basics of Wireshark and Sniffing on the network

## Slide 3: Analyzing a TCP Session
Open Wireshark and go to CaptureInterfaces. Select an appropriate Network Interface Card and press Start to begin capturing packets.
Wireshark will start capturing all the packets on LAN, whether these are destined for or originating from your PC or not!
Now apply a filter to capture TCP packets only. Also apply another filter so that you can see only the traffic destined for or originating from your PC. Here is the composite filter string
(ip.src==your_ip_addr|| ip.dst==your_ip_addr) && tcp
Here “II” stands for logical OR and “&&” stands for logical AND.

## Slide 4: Analyzing a TCP Session
Open command prompt and establish an ftp session to an FTP server. For this lab, an FTP server has been established at 192.168.25.169. At home, you can use ftp.mozilla.orgas FTP server. Coming back to FTP session, type following commands in command prompt to setup a session:
  Type ftp 192.168.25.169
  Enter your first name as username
  Give an arbitrary password. You will not be authenticated with these credentials; however this is sufficient for analyzing a TCP session.
  Type bye to end up the ftp session.
Now go back to Wireshark and stop capturing packets by going to Capture  Stop.
Look for the three-way handshake packets (SYN, SYN/ACK, ACK) and click on the SYN/ACK packet to view its details.

## Slide 5: Analyzing a TCP Session
Examine the IP header, compared to the discussion. Look for the following:
  Which IP version this session used? IPv4 or IPv6?
  What is the value of time-to-live field?
  What is the upper layer Protocol ID?
  What is the source IP address?
  What is the destination IP address?
Expand the TCP segment and answer the following:
  What is the source port?
  What is the destination port?
  Which TCP header flags are set?
  What is the window size?

## Slide 6: Analyzing a TCP Session
Now scan through some data packets and see what is contained in FTP message. Expand some FTP messages and try reading what’s inside them.
Can you find packets originating from your PC to FTP server that contained your username and password? Do you think FTP uses safe authentication procedures? If not, why not?
Now look for the tear down packets. Was the tear-down graceful or ungraceful?
Once again go back to Wireshark and Start capturing. Now open some browser and open any favorite website. Apply httpfilter in wireshark and see how packets are being transacted while you browse through the webpage.

## Slide 7: Analyzing a TCP Session
Filter String:(ip.src==your_ip_addr || ip.dst==your_ip_addr) && http
You can even find the packets containing complete images with in the webpage. You may encounter some ungraceful tear-downs. Also notice that request to just one URL may result in multiple TCP sessions.

## Slide 8: Analyzing ICMP
Open Wireshark and go to CaptureInterfaces.Select an appropriate Network Interface Card and press Start to begin capturing packets.
Now apply a filter to capture ICMP packets only.
Filter String:(ip.src==your_ip_addr || ip.dst==your_ip_addr) &&icmp
Ping some PC in the lab or simply your Default Gateway.
After the ping is complete, go back to wireshark and stop capturing.
Click on the ping request packet and expand the ICMP message in the packet details pane. What is the value of Typefield and what does it indicate?

## Slide 9: Analyzing ICMP
Click on the ping reply packet and expand the ICMP message in the packet details pane. What is the value of Typefield and what does it indicate?
Click on Data field of ICMP ping request packet and observe its ASCII value in “Packets Byte Pane” (the lower most section), what is it containing?
Answer the questions asked throughout the manual and submit it as lab report of today’s lab session. Name the file in the format Lab 11 -NC <First_name Last_name>.